2024 SKILLS AUTO BODY REPAIR

WELDING

(general instructions)

Structural Panel Sectioning Project

Task Sheet Project “A”

READ ALL INSTRUCTIONS BEFORE BEGINNING

Duration: 3 Hours

This Project will test your ability to perform a sectioning procedure on simulated panels, following industry-acceptable standards. The completed project will be evaluated for the quality of your work based on the technical accuracy of your measurements and welds and the appearance of the completed section.

Materials: *Each competitor will receive only one Project Panel component.

*NO exceptions!

Students will cut simulated components to create: 1 (one) Vehicle and 1 (one) Salvage panel. The “short piece” that is cut off at the beginning of the competition will become your “Salvage Component.”

## General Overview

Each Competitor has been provided with one simulated “B’ Pillar.

You will be trimming the component to create the following:

1 long section – VEHICLE component

1 short section – SALVAGE component

You are asked to cut and section the project according to the instructions provided.

The project pieces must be welded together as per industry standards.

To avoid confusion, one piece is identified as the Vehicle Component and the other piece as the Salvage Component.

Note that the project components are also identified for Top.

All corrosion protection must be replaced.

# Completed VEHICLE project panel to be presented to the exam marker.